## Slide 1: Eval15

## Slide 2
A.M.M. Schreurs, X. Xian, L.M.J. Kroon-Batenburg,
J. Appl. Cryst. (2010). 43, 70-82.

## Slide 3: help
Typing “help” will open a webpage with the manual.
Typing “help commandname” will open a webpage with the manual entry for the commandname. Example: “help focus”

## Slide 4: Diffraction geometry
90-q
rotation axis
2q
d*hkl

Ewald sphere
Area detector
1/
2d sinq = l

## Slide 5: General impact
focus
90-θ
ω
rotation to Bragg condition at ζ:
central impact
cos z = (sin q-sin cfk)/(cos cfk cos c)
crystal size and shape
mosaic spread
wavelength
k,m
1/λ
2d sin =n

## Slide 6: Least squares (SVD)
Standarddeviation of interated reflection
Standarddeviation of interated reflection
Standard deviation of integrated reflection
Variances and co-variances available

## Slide 8: Configuration files
detector.pic
focus.pic
refine.pic
simulation.pic
spectrum.pic
crystal.pic
mosaic.pic
[eval15.init]

## Slide 9: Read boxfile
The command “read” opens a boxfile
Example: read 1 100 opens the first boxfile reads reflection number 100 displays the reflection graphically

## Slide 10: pq
With the command “pq” the program will search for the next reflection with I/s>10
reflections with error flags (overflow, overlap, etc.) will be skipped

## Slide 11: Refinement variables
The command “free” makes a variable refinable
Example: free mosaic
Only useful to determine parameters for the configuration files
For the final intensity determination, use only free shextra

## Slide 12: refine
With the command “refine” all free variables are refined
Target function: fombox

## Slide 13: onescan
The command “onescan” iterates a variable from startvalue to stopvalue
Example: refine (to refine impact position) distribution type onescan distribution plot onescan mosaic 0.05 0.1 1.0 (increment 0.05, startvalue 0.1, stopvalue 1.0)

## Slide 14: onescan
Minimum at mosaic = 0.25 for this reflection

## Slide 15: mosaic
The description of the mosaicity is given in the file mosaic.pic
  Isotropic mosaicity
  Anisotropic mosaicity (animo, anivec)
With mosaicadd you can prepare a “mosaicity spectrum”
The “mosaic spectrum” is a possibility to handle cracked crystals.

## Slide 16: spectrum
The X-ray spectrum of the primary beam is described in the file spectrum.pic
You can add additional wavelengths using the command “lamdaadd”
The command “show lambda” prints the current values
With “distribution type lambda” and “distribution plot” you obtain a graphical output.

## Slide 17: distribution plot

## Slide 18: printslices
With the command “printsclices” it is possible to print pixel intensities on the screen
Example: printslices simulated on go
With “slicewrite” you can write the pixel intensities to a file

## Slide 19: printslices

## Slide 21
program “refl3d” (part of the Eval suite)