## Slide 1: Eval15 integration
Martin Lutz Crystal and Structural Chemistry Bijvoet Center for Biomolecular Research Utrecht University The Netherlands
m.lutz@uu.nl
http://www.cryst.chem.uu.nl/lutz

## Slide 2
A.M.M. Schreurs, X. Xian, L.M.J. Kroon-Batenburg,
J. Appl. Cryst. (2010). 43, 70-82.

## Slide 3: Introduction
Academic development
Aim: meet the requirements of the researcher
Aim: data quality
Aim: deal with “standard” cases
Aim: deal with “difficult” cases
Lower priority: user interface
Lower priority: speed

## Slide 4: General impact
focus
90-θ
ω
rotation to Bragg condition at ζ:
central impact
cos z = (sin q-sin cfk)/(cos cfk cos c)
crystal size and shape
mosaic spread
wavelength
k,m
1/λ
2d sin =n

## Slide 5: Program flow

## Slide 6
view
eval15
any
refl. data, cell parameters
final.y
boxfiles
orientation matrix
configuration files
configuration files
raw images

## Slide 7: view
View raw images
Peak search
Create boxfiles
Helper applications

## Slide 8: configuration files for “view”
detalign.vic
goniostat.vic
beamstop.vic
[view.init]

## Slide 9: Peak search with “view”
Create macro files for “view” using buildsearch
view @isearch
Result files:
  name.drx
  name.pk

## Slide 10: dirax
Indexing program
A.J.M. Duisenberg (1992). J. Appl. Cryst. 25, 92-96
Input file:
  name.drx
Result file:
  name.rmat

## Slide 11: peakref
Refinement of orientation matrix and diffractometer configuration
Input files:
  name.rmat
  name.pk
Result files:
  name.rmat
  detalign.vic, goniostat.vic

## Slide 12: rmatrix
Find standard setting of unit cell (Bravais centering)
Input file:
  name.rmat
Output file:
  name.rmat

## Slide 13: Create boxfiles with “view”
Create macro files for “view” using builddatcol
view @datcol
Result files:
  *.shoe

## Slide 14: Integrate the boxfiles
Create Eval15 configuration files with buildeval15
Interactively check the profile prediction with eval15
Integrate all boxfiles with eval15all

## Slide 15: “Parallel processing”
You can use different processors for the integration
Create a file ~/hosts which contains the computernames for login with ssh (with passkey)
Alternatively create a file “computers” in the local directory
batchsetup set
batchstart

## Slide 16: Queing system
If you are using Eval15 regularly on a computer cluster, we recommend to use the gridengine (probably included in your linux distribution)

## Slide 17: any
any read final.y.gz
hklf4 (writes reflections in SHELX format)
pk (writes impact positions for peakref)

## Slide 18: Helper programs related to “view”
tunebeamstop
scancheck / scancheckplot
buildscc / scanplot
imagesum
low3
buildrest
buildphichi

## Slide 19: Helper programs related to unit cell
rmatrix
cell
cellplot
2view
p4p2rmat

## Slide 20: Helper programs for reflection data
anafcf
loglog
mergehklf5
plotcosines