## Slide 1: peakref

## Slide 2: Introduction
Refinement of unit cell parameters and orientation matrix
Refinement of diffractometer parameters
Constraints are available

## Slide 3: help
Typing “help” will open a webpage with the manual.
Typing “help commandname” will open a webpage with the manual entry for the commandname. Example: “help go3”

## Slide 4: rmat
The command “rmat” reads the orientation matrix from a file
If the rmat-file contains information about the point group, constraints are set accordingly
With the commands “rmat2”, “rmat3”, etc. It is possible to read additional orientation matrices

## Slide 5: pk
The command “pk” reads a file with the impact positions
With the commands “pk2”, “pk3”, etc., additional files can be read
If the pk-file originates from a peak-search, reflections are not indexed
If the pk-file originates from an Eval15 integration, reflections are indexed

## Slide 6: hklreind/reind
By default, the program peakref does not re-index reflections
With the commands “hklreind” and “reind” the user can change this behaviour

## Slide 7: free/fix
With the commands “free” and “fix” the user selects the parameters which are (not) refined.

## Slide 8: status
The command “status” shows the current values of parameters
It also shows if a parameter is free or fixed

## Slide 9: go
The command “go” performs the refinement
The command “go3” performs 3 cycles of refinement

## Slide 10: byexperiment
The command “byexperiments” allows the parameter to have a different value for every experiment (“scan”)

## Slide 11: reject
Largely deviating reflections are not used in the refinement (“forbid” flag)
It depends on the average residues resmm (mm residue) and resrot (rotation residue). Deviating means f*resmm and f*resrot Example: reject 5 (this means f = 5.0)
If the refinement improves, more reflections should fit
On the other side, during refinement resmm and resrot become smaller. Therefore a smaller deviation will flag the reflection as “forbid”.

## Slide 12: Saving results
save: new file “detalign.vic”
savermat: new rmat-file
save gonio: new file “goniostat.vic”

## Slide 13: reportsigma
The command “reportsigma” writes the current cell parameters and their standard uncertainties into the file peakref.lis