## Slide 1: view

## Slide 2: help
Typing “help” will open a webpage with the manual.
Typing “help commandname” will open a webpage with the manual entry for the commandname. Example: “help drawbeamstop”

## Slide 3: Image formats
Nonius KappaCCD
ADSC
Image-Cif
Mar
MarCCD
Agilent
Rigaku-Raxis
Bruker Smart

## Slide 4: read
The command “read” reads a diffraction image and interprets its header

## Slide 5: plot
The command “plot” generates a graphical display

## Slide 6: rmat
The command “rmat” reads an rmat-file containing the orientation matrix
With the commands “rmat2”, “rmat3”, etc. you can read additional orientation matrices

## Slide 7: datcol
The command “datcol” shows the predicted impact positions based on the orientation matrix.

## Slide 9: go
The command “go” opens a graphical menu
A <right-mouse-click> in the main window closes the graphical menu

## Slide 11: Primary beam
The detector alignment is essential for the correct use of the Eval suite
With the command “markprimary” the impact of the primary beam is displayed
With the command “setprimary” a different impact position of the primary beam is chosen
With the command “save detalign” a new calibration file is written to the disk

## Slide 12: profilerad
The command “profilerad” creates a radial profile
(“powder diagram”)
Tip: use first the command “profilexy”. Then the command “profilerad” will write into a file

## Slide 14: External programs based on “view”

## Slide 15: Imagesum
Example: imagesum read s01f*.sfrm write sum.sfrm
Use of “view”: view read sum.sfrm plot max mode equal plot

## Slide 17: tunebeamstop
“tunebeamstop” is a GUI to optimize the beamstop description
Note: the GUI only uses a subset of available commands
The full set of commands is available in “view”. Use “save beamstop” to write the file beamstop.vic

## Slide 19: img2r
The program “img2r” reads a set of images and prepares a reciprocal space reconstruction.
The ‘’coot” software is needed for display